## Slide 1: Smartphone localization
Shuailing Yang

## Slide 2: Outline
Beepbeep
Phone to phone
Our method

## Slide 3: Problem description
We use location
information of anchor phone to estimate the
location of the unknown
nodes.
Anchor phone
Unknown nodes
?
Localization need the information of distance and angle

## Slide 4: Distance measurement
Mostly, based on time-of-arrive measurement
  Sound often chosen
  Slower speed => less demanding on time accuracy
  Distance = speed x time()
t1
t2
t3
t4

## Slide 5: The root cause of time inaccuracy – three uncertainties
Clock synchronization uncertainty
Sending uncertainty
Receiving uncertainty
time
...
t0 = loc_clock();
write(sound_dev, signal);
...
software issuing command
sound leaves
speaker
unknown delays (software, system, driver, hardware, …)
...
read(sound_dev, signal);
t1 = loc_clock();
...
software aware of arrival
sound
reaches mic
unknown delays (hardware, interrupt, driver, scheduling, …)
?
?

## Slide 6: Effects of uncertainties
Example measurement of the lower bound on COTS mobile devices (HP iPAQ rw6828)
  Highly fluctuating, appears unpredictable
  Easily adds up to 1-2 ms
CPU idle
CPU heavily loaded

## Slide 7: Beepbeep’s basic procedure
Device A
Device B
A’s recording
B’s recording
ETOAA
ETOAB
Device A emits a beep while both recording
Device B emits another beep while both continue recording
Both devices detect TOA of the two beeps and obtain respective ETOAs
Exchange ETOAs and calculate the distance

## Slide 8: Mathematical derivation
tA3
2nd Beep
tB3
tB2
1st Beep
tB1
tA0
tA1
ETOAA
ETOAB
D= ·(ETOAA-ETOAB)
= ·((nA3-nA1) - (nB3-nB1))
ETOAA= (nA3-nA1)/fA
ETOAB= (nB3-nB1)/fB

## Slide 9: BeepBeep Summary
Advantage : accurate, error in cms
Disadvantage: distance measurement only

## Slide 10: Phone-to-phone 3D localization
Idea:
Use multiple microphones & sensors on the phone

## Slide 11: Motivation
Example:
Face-to-face sword fight game between phone users
Other examples:
Ping-pong type game
Positioning for combining displays
...
Notes: revise motivation slide to include additional examples

## Slide 12: Design overview
Initialization
  Perform loose time sync
Exchange acoustic tones
  Record accelerometer and compass measurements
Calculate distance and angle measurements
  Two types of acoustic cues
  Exchange measurements
4. Estimate position

## Slide 13: Time-of-arrival cues
Time-of-Arrival Cues
Distance:
Angle:
E
C
F
B
D
A
Speaker C
Mic A
Mic B
O

## Slide 14: Power cues
Power Cues
Observation: two mics experience different attenuation of received signal power
Create look-up table that maps power ratios to angle θ
E
C
F
B
D
A
Speaker C
Mic A
Mic B
O

## Slide 15: conclusion
3D localization with just two regular phones by combining available sensors
  90th percentile accuracy: 13.9cm
  50th percentile accuracy 4.9cm
Localization many phones?

## Slide 16: Questions
tA3
2nd Beep
tB3
tB2
1st Beep
tB1
tA0
tA1
3rd Beep
?
How to distinguish between the second Beep and the third Beep ?
How to localization the third phone , and even more phones?

## Slide 17: Our method
FM radio frequency
Beep
ETOA
tA0
tB1
tB2
Distance = ETOA * SoundSpeed
Calculate distance:

## Slide 18: How to Compute the ETOA

## Slide 19: Angle measurement
Speaker
Mic A
Mic B
arcos(
TDOA
The distance between the two mics AB is constant.

## Slide 20: Region overlap
Mic B
Mic A
Mic E
Mic D
Anchor 1
Anchor 2
We can used region overlap to
improve localization accuracy.

## Slide 21: Future work
Algorithm Analysis, likes localization accuracy, computational complexity
Measured performance

## Slide 22: Thanks
questions?